## Slide 1
PROJECT OBJECTIVES
AEGIS-172: cloud-adaptive two-player radar defense arena
A standalone embedded game system that combines physical scanning, asymmetric controls, and AWS-driven missions.
What we are building
CC3200-led tabletop arena with OLED HUD, real-time radar sweep, servo shield control, and cloud-scored competitive rounds.
Why it stands out
Instead of a lock, tuner, or simple arcade clone, the system blends mechatronics, two-player interaction, and AWS mission generation in one standalone device.
3
AWS services in critical path
5+
sensors fused into threat score
2
MCUs split by timing domain
Comparable products and our difference
Closest references: radar toys, reaction games, and simple home security prototypes
Our pivot adds competitive two-player roles instead of passive monitoring
Mission scripts come from AWS IoT + Lambda + S3 instead of fixed local levels
Replay artifacts and leaderboard data make the demo measurable and reproducible
Presentation plan
1 slide objective, 2 slides architecture/tasks, 2 slides progress + demo evidence
AEGIS-172 | EEC172 Final Project
Slide 1 | Objectives

## Slide 2
SYSTEM MODULES
Block diagram: data flow, control flow, and cloud path
The project splits deterministic hardware control onto the UNO while the CC3200 owns UI, state, and cloud traffic.
Aktan lead
Gezheng lead
Shared
CC3200 Main Controller
match state machine
OLED HUD + scoreboard
AWS IoT / Lambda / S3 client
UART control exchange
Aktan lead
UNO Coprocessor
stepper sweep + ultrasonic sectors
servo, RGB, buzzer outputs
sensor frames back to CC3200
Gezheng lead
Player Inputs
Joystick: defender shield placement
Start button: local round control
Attacker Channel
IR remote injects actions
Asymmetric two-player interaction
AWS Path
IoT: mission request + telemetry
Lambda: scoring + mission generation
S3: replay and leaderboard artifacts
Physical Arena
stepper + ULN2003 radar head
ultrasonic, tilt, light, DHT11
servo shield, buzzer, RGB
analog
IR
TLS
UART
control
missions
AEGIS-172 | EEC172 Final Project
Slide 2 | Architecture

## Slide 3
TASK MODULES
Ownership map and dependency flow
Color coding matches the team member leading each task, with shared integration work shown separately.
Aktan lead
Gezheng lead
Shared
Aktan
Shared integration
Gezheng
Now
CC3200 game loop
replace ParkPilot modes with round states
OLED radar HUD and scoring view
Next
AWS pipeline
IoT shadow schema
Lambda mission + score handlers
Done
Presentation + website
deck, report, webpage polish
final evidence packaging
Done
UART frame contract
half-duplex control/sensor exchange
reuse same protocol for CC3200 swap
Now
System integration
power stability, level shifting, task timing
full round validation
Planned
Demo choreography
4-minute script, clean wiring, recovery path
video capture and judge-facing proof
Now
UNO mechatronics
stepper sweep, servo shield, buzzer, RGB
joystick and IR local handling
Now
Sensor fusion inputs
ultrasonic, tilt, light, DHT11
noise-aware sampling
Next
Reliability pass
stable 5V rail and wiring cleanup
repeatable live demonstration behavior
AEGIS-172 | EEC172 Final Project
Slide 3 | Tasks + Ownership

## Slide 4
PROGRESS REPORT
Current status, remaining work, and finish timeline
The goal is to enter lecture with a local playable build first, then lock cloud and polish second.
Completed
Project pivot finalized: AEGIS-172 concept, site rewrite, proposal, and architecture
Dual-UNO prototype path established with working request/response UART frame contract
Local state machine, joystick shield control, stepper sweep, and actuator loop verified
In progress
CC3200 master port from existing ParkPilot firmware and OLED HUD redesign
UNO sensor wiring cleanup and final pin map for joystick, IR, ultrasonic, tilt, light, DHT11
Scoring balance so threat level, buzzer, and RGB are readable in demo conditions
Planned next
AWS IoT mission request, Lambda scoring, and S3 replay artifact integration
Demo video capture, enclosure cleanup, and fallback local mission mode
Final lecture script and live verification checklist
Tonight
stabilize local game loop and presentation
Tomorrow
swap in CC3200 and light up OLED HUD
Next 48h
wire AWS mission + replay path
Before lecture
record clip and rehearse 4-minute run
AEGIS-172 | EEC172 Final Project
Slide 4 | Progress

## Slide 5
PARTIAL DEMO
Demo slot plus speaking cues for the lecture presentation
This slide is structured for the required 10-15 second clip and a quick verbal walkthrough of what is already working.
Insert 10-15s partial demo clip here
Suggested sequence: boot -> sweep -> shield move -> score update -> cloud request overlay
Current verified pieces
master-coprocessor UART loop
state transitions and score ticks
stepper radar sweep + joystick shield motion
presentation website and architecture
What to narrate over the clip
boot from flash with no host control
defender shield tracks joystick sector
ultrasonic sweep drives threat pressure
same frame contract will move to CC3200 + AWS
Before class: replace the placeholder with a real MP4 clip from the prototype. The rest of the slide is ready.
AEGIS-172 | EEC172 Final Project
Slide 5 | Demo Placeholder